## Slide 1
ARC COMPANION
SOFTWARE ARCHITECTURE & CODE
Arduino Uno R3 Embedded Systems | GitHub Repository
Complete Code Walkthrough & Architecture Documentation

## Slide 2
SOFTWARE ARCHITECTURE
Complete System Overview
SETUP()
Pin config
Interrupts
Serial init
DATA STRUCTS
Blueprints
Stats
Menu State
CONTROL
8 Buttons
2 Knobs
Debounce
MENU SYSTEM
State machine
Navigation
Actions
OUTPUT
4 LEDs
Serial
Buzzer
All components run in MAIN LOOP (~50-100 times per second)
LOOP CYCLE: Read Inputs → Process → Update State → Output → Display

## Slide 3
PIN CONFIGURATION
Arduino Uno R3 - All Connections
BUTTON INPUTS
Pin 2 (INT0) → MENU button [Interrupt]
Pin 3 (INT1) → SELECT button [Interrupt]
Pin 4 → BACK button [Poll]
Pin 5 → ACTION button [Poll]
Pin 6-9 → UTILITY buttons 1-4 [Poll]
ANALOG INPUTS
A0 → KNOB_LEFT (0-1023) → Menu navigation
A1 → KNOB_RIGHT (0-1023) → Value adjust
Mapped to application-specific ranges
LED OUTPUTS
Pin 12 (LED_BLUE) → Power indicator
Pin 13 (LED_GREEN) → Active indicator
Pin A4 (LED_RED) → Alert indicator
Pin A5 (LED_YELLOW) → Activity indicator
SPECIAL OUTPUTS
Pin 11 → RGB Underglow (WS2812B data)
Pin 10 → Piezo Buzzer (audio feedback)
USB → Serial communication (9600 baud)

## Slide 4
DATA STRUCTURES
Core C++ Structs & Variables
struct Blueprint
char name[30] // Max 30 chars
byte rarity // 0-3 (Common-Epic)
char location[20] // Where to find
byte components // Quantity needed
boolean discovered // Player found it?
struct GameStats
uint16_t raids_completed
uint16_t raids_successful
uint32_t total_playtime
byte blueprints_found
uint16_t best_raid_time
enum MenuState
STATE_HOME → STATE_BLUEPRINTS → STATE_SEARCH → STATE_RAID_TIMER → STATE_STATS → STATE_LED_CONTROL → STATE_SETTINGS → Back to HOME
5 demo blueprints stored in PROGMEM (program memory)

## Slide 5
MAIN CODE SECTIONS
Key Functions & Their Purpose
INITIALIZATION
void setup() - Runs once on power-up
void initializeEEPROM() - Load saved game data
void setupInterrupts() - Enable INT0/INT1
INPUT HANDLING
void handleMenuButton() - Fast interrupt response
void handleButtonInput() - Poll-based reading
int readAnalogKnobs() - Get rotation 0-1023
CORE LOGIC
void loop() - Main runtime (50-100x/sec)
void updateMenuState() - Process state changes
void updateRaidTimer() - Countdown tracking
OUTPUT & DISPLAY
void updateStatusLEDs() - Update 4 indicators
void displayMenu() - Serial output
void controlUnderglowLED() - RGB effects

## Slide 6
BUTTON HANDLING SYSTEM
Two-Method Approach
INTERRUPT-DRIVEN (Pins 2 & 3)
✓ Called IMMEDIATELY on press
✓ MENU & SELECT buttons (critical)
✓ <2ms response time
✗ Must be brief (no delays)
✗ Can't do complex ops
POLLING (Pins 4-9)
✓ Read every loop cycle (10-20ms)
✓ BACK, ACTION, UTILITY buttons
✓ Can perform complex operations
✗ Slight response delay
✓ Safe for game logic
DEBOUNCING: 20ms delay prevents multiple triggers from button bounce/contact chatter
Problem: Physical button pressed → Electrical noise → Multiple triggers detected
Solution: Read button → Wait 20ms → Read again → If still pressed, count as 1 press

## Slide 7
ANALOG INPUT: ROTARY KNOBS
Mapping Physical Rotation to Data
Potentiometer Reading
int value = analogRead(A0); // Returns 0-1023
// 0 = fully CCW
// 512 = middle
// 1023 = fully CW
Mapping to Application
// Map to menu items
int menu_pos = map(value, 0, 1023, 0, 5);
// value: 0-1023
// menu_pos: 0-5 (6 items)
// Application:
// Knob LEFT → Menu navigation
// Knob RIGHT → Value adjustment
KNOB CONTROL FLOW
Read analogRead() → Map to range (0-1023 → 0-5) → Update menu position → Refresh display → User sees change
Analog resolution: 10-bit (1024 levels) | Update rate: ~10ms per sample

## Slide 8
STATE MACHINE LOGIC
How Menu Navigation Works
enum MenuState Definitions
STATE_HOME → Boot/idle screen
STATE_BLUEPRINTS → Browse found blueprints
STATE_SEARCH → Search blueprint database
STATE_RAID_TIMER → Active raid countdown
STATE_STATS → View game statistics
STATE_LED_CONTROL → Adjust LED colors
STATE_SETTINGS → Device configuration
State Transitions
In loop():
if (menu_button_pressed) current_menu++;
if (select_button_pressed) enterMenu();
if (back_button_pressed) current_menu = STATE_HOME;

## Slide 9
RAID TIMER SYSTEM
Real-Time Countdown Tracking
struct RaidTimer
boolean active; // Running?
unsigned long start_time; // When started
unsigned long duration; // Total seconds
unsigned long elapsed; // Elapsed so far
Update Logic
if (raid_active) {
elapsed = (millis() - start) / 1000;
if (elapsed >= duration) {
active = false; // Complete
recordStats();
}
}
TIMER CONTROL FLOW
1. User starts raid → Record start time (millis()) → Set duration (120 sec) → Set active=true
2. Each loop: Calculate elapsed = (current time - start time)
3. Display: "45/120 seconds" → LED pulses → Yellow indicator blinks
4. Timer complete: Stop → Update stats → Sound alert → Save to EEPROM

## Slide 10
LED STATUS INDICATORS
4-Color Communication System
BLUE (Pin 12)
Power Status
Always ON when powered
GREEN (Pin 13)
Device Active
ON when using menus
RED (Pin A4)
Alert/Warning
ON if error detected
YELLOW (Pin A5)
Activity
PULSES during raid timer
LED CONTROL CODE
void updateStatusLEDs() {
digitalWrite(LED_BLUE, HIGH); // Always on
digitalWrite(LED_GREEN, (current_menu != HOME) ? HIGH : LOW);
digitalWrite(LED_RED, error_flag ? HIGH : LOW);
digitalWrite(LED_YELLOW, raid_active ? HIGH : LOW);
}

## Slide 11
MAIN LOOP EXECUTION
What Happens Every 10-20ms
Simplified Loop() Pseudocode
void loop() {
// 1. READ ALL INPUTS
readButtonStates(); // Pins 2-9
readAnalogKnobs(); // A0, A1 → 0-1023
// 2. UPDATE STATE
updateMenuState(); // Process button input
updateRaidTimer(); // Count down if active
// 3. CALCULATE OUTPUT
calculateStatusLEDs(); // What LEDs should show?
// 4. SEND OUTPUT
updateStatusLEDs(); // Write to pins 12, 13, A4, A5
displayMenuOutput(); // Serial output to USB
delay(10); // 10ms cycle ≈ 100Hz loop frequency
}

## Slide 12
SERIAL COMMUNICATION
USB ↔ Computer (9600 Baud)
Data Flow
Arduino → USB → Serial Monitor (Arduino IDE) or Any Terminal (Putty, etc.)
Baud Rate: 9600 | Data Bits: 8 | Parity: None | Stop Bits: 1
Example Output Sequence
▲ ARC COMPANION ▼
Menu
>
Blueprint Search
? cannon
Found: Energy Cannon Barrel | EPIC | 3 components
Start Raid? [Y/N]
Raid Timer: 5/120 seconds
Raid Timer: 10/120 seconds
...
Raid Complete! Stats updated.

## Slide 13
COMPLETE USER INTERACTION FLOW
Step-by-Step Integration
1. POWER ON → setup() → All pins configured, interrupts enabled, EEPROM loaded, "Ready" → Blue LED on
2. USER PRESSES MENU → INT0 interrupt fires → currentMenu++ → Green LED on → Serial output
3. LOOP RUNS 100x/sec: Reads buttons → Checks if select pressed → Updates menu → Outputs to LEDs/Serial
4. USER ROTATES KNOB → analogRead() returns 0-1023 → map() to 0-5 → menu_position = new value
5. USER PRESSES SELECT → INT1 fires → enterMenu() → Load blueprint data → Display blueprint
6. USER PRESSES ACTION (Start Raid) → raid_timer.active=true → raid_timer.start_time=millis()
7. MAIN LOOP UPDATES TIMER: elapsed = (millis() - start) / 1000 → "45/120 sec" → Yellow LED pulses
8. RAID COMPLETE (120 sec): active=false → stats.raids_completed++ → saveToEEPROM() → Red alert blink
9. POWER DOWN → All data saved → Ready for next session with progress intact

## Slide 14
GITHUB REPOSITORY
github.com/arc-companion-arduino
Complete documentation includes:
✓ Full Arduino sketch with 520+ lines of commented code
✓ Detailed README with architecture diagrams
✓ Pin configuration and wiring guide
✓ Code examples for extending functionality
✓ Performance specifications and benchmarks
✓ Troubleshooting guide